## Slide 1
PRAKALP
Name: Kavya Hegde USN:01FE20BEC093
Project: 7 pack opamp design
Notes: 1

## Slide 2: Design Details
Cell Name | 7_pack_opamp
Test Bench Name | 7_pack_opamp_test
Technology | 180nm TECHNOLOGY UMC_18_CMOS
Devices | MOSFET, CAPACITORS, VOLTAGE AND CURRENT SOURCE
Simulation Area | CADENCE
Design Owner | Kavya Hegde
Reviewed By | -
Acknowledging | Dr. SUJATA KOTABAGI , SCHOOL OF ELECTRONICS AND COMMUNICATION

## Slide 3
Contents
Design Details
Pin Description
  Simulation plan
SCM
Schematic
  Test bench
  DC analysis
  AC analysis
Notes: 3

## Slide 4: Two Stage Amplifier
High gain and high output swing
1st stage : Differential amplifier
2nd stage: Common source with PMOS load , capacitive load
Overall gain Av=A1*A2
Negative feedback increases oscillations
Need for greater PM

## Slide 5: Two Stage Amplifier
OP-AMP COMPENSATION :
2 pole system
PM closes zero
Millers Compensation
Cc between the outputs of two stages
Pole splitting
Dominant pole compensation
P1=1 ÷ gm7R1R2Cc

## Slide 6: Pin Description
THE MAIN PURPOSE IS TO SHOW THE BASIC METHODS FOR DESIGNING A TWO STAGE OP-AMP BASED ON CADENCE, AND DC SCHEMATIC PLOT AND AC ANALYSIS SIMULATION.
Sl.No | Pin Name | Description | Input/Output/Supply
1 | VDD | Supply pin VDD | Supply
2 | GND | Supply pin GND | Supply
4 | Iref | 20µA of reference current | Input
5 | V+ | +ve Input | Input
6 | V- | -ve Input | Input
7 | VOUT | Output voltage | Output

## Slide 7: 7_pack SCM
7_pack SCM |  |  |  |  |  |  |  | 
Specification Compliance Matrix |  |  |  |  |  |  |  | 
Parameter | Unit | Specification |  |  | PVT |  |  | Comment
 |  | Min | Typ | Max | Min | Typ | Max | 
VDD | V | 1.8 | 1.8 | 1.8 | 1.8 | 1.8 | 1.8 | Supply Voltage
TEMP | °C | -40 | 27 | 125 | -40 | 27 | 125 | Temperature
Iref | µA | 20 | 10 | 20 | 20 | 10 | 20 | Reference Current
ICMR | V | 0.8 | 0.7 | 1.6 | 0.8 | 0.7 | 1.6 | Input Common Mode Range(ICMR)
CL | pF | - | 2 | - | - | 2 | - | Load Capacitance
Gain | dB | - | 60 | - | 66 | 60 | 60.74 | DC gain
PM | deg | - | 60 | - | 57 | 55 | 58.34 | Phase Margin
GBW | MHz | - | 30 | - | 32.2 | 30 | 32.76 | Gain Bandwidth Product

## Slide 8: Schematic
HAND CALCULATIONS ARE BEEN DONE TO OBTAIN THE DESIGN PARAMETERS (I.E.(W/L) RATIO).

## Slide 9: Bias Parameters
Parameter | M1 | M2 | M3 | M4 | M5 | M6 | M7 | M8
W (µm) | 3 | 3 | 7 | 7 | 12 | 87 | 75 | 12
L (nm) | 500 | 500 | 500 | 500 | 1000 | 500 | 1000 | 1000
Vgs (V) |  |  |  |  |  |  |  | 
Vds (V) |  |  |  |  |  |  |  | 
Bias parameters

## Slide 10: AC Analysis Gain-Phase Plot-Vin=0.8V Gain=66dB,BW=32.20MHz,PM=57degree

## Slide 11: AC Analysis Gain-Phase Plot-Vin=1.6V Gain=60.74dB,BW=32.76MHz,PM=58.34degree

## Slide 12: Power Dissipation
Total Power=Vdd*Sum of all currents
=1.8*(125+20)
=261uW
For Vin=0.8V
Power=273.53uW
For Vin=1.6V
Power=297.88uW

## Slide 13: Thank You
20